## Slide 1: The Little-Man Computer
Damian Gordon

## Slide 2: The Little-Man Computer
Most computer architectures conform to the so-called von Neuman Architecture. This means that they execute programs by accessing both instructions and data on the same storage device. The computer performs the following sequence of steps;

## Slide 3: The Little-Man Computer
Fetch the next instruction from memory at the address in the program counter
Decode the instruction using the control unit
Increment the Program Counter
The control unit commands the rest of the computer to execute the instruction
Go to step 1

## Slide 4: The Little-Man Computer
This is the Fetch-Decode-Execute (FDE) cycle. These computers are known as Stored-Program Computers since the separation of storage from the processing unit is implicit in this model.

## Slide 5: The Little-Man Computer
A conceptual device or thought experiment to teach this architecture was developed by Stuart Madnick of MIT in the 1960s and is called the Little Man Computer (LMC) Paradigm.

## Slide 6: The Little-Man Computer
The LMC Paradigm consists of a room with a 'Little Man' (or homunculus) who simulates the operations of a computer. The room has an array of locations that store information (and instructions), an input and output tray, and a calculator.

## Slide 7: The Little-Man Computer
The analogy between the LMC and real computers is not perfect, but this approach is a simple and powerful conceptual model which allows us easy entry level to the basics of computer architecture.

## Slide 8
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
1
2
3
4
5
6
7
8
0

## Slide 9
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
Pigeon Holes
1
2
3
4
5
6
7
8
0

## Slide 10
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
In-tray
1
2
3
4
5
6
7
8
0

## Slide 11
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
Program
Counter
1
2
3
4
5
6
7
8
0

## Slide 12
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
Calculator
1
2
3
4
5
6
7
8
0

## Slide 13
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
Out-tray
1
2
3
4
5
6
7
8
0

## Slide 14
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 15
9
10
11
12
13
14
15
16
18
19
1
2
3
4
5
6
7
8
0
The addresses of the pigeon-holes are consecutive, and they may contain either:
  Data (numbers, values), or
  Instructions (copy, subtract, add)
17
20

## Slide 16
In-tray
Out-tray
--
Each morning the boss fills the pigeon-holes with several instructions and data, and puts papers in the IN-TRAY

## Slide 17
In-tray
Out-tray
--
The Little Man’s job is to read these instructions one at a time, reading the corresponding instruction to the value on the Program Counter.

## Slide 18
In-tray
Out-tray
--
The calculator (aka Accumulator) can be used to store values temporarily, and do arithmetic (add, subtract, etc.).

## Slide 19
In-tray
Out-tray
--
The Little-Man will output all of his results into the OUT-TRAY which the boss collects in the evenings.

## Slide 20
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
1
2
3
4
5
6
7
8
0

## Slide 21
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
1
2
3
4
5
6
7
8
0
STORE

## Slide 22
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
1
2
3
4
5
6
7
8
0
STORE

## Slide 23
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
-
19
1
2
3
4
5
6
7
8
0
STORE
LOAD

## Slide 24: The Little-Man Computer
TYPE OF INSTRUCTION | INSTRUCTION | DESCRIPTION
Arithmetic | ADD | Add the value of a given memory location to calculator
Arithmetic | SUBTRACT | Subtract the value of a given memory location to calculator
Data Movement | STORE | Copy the value from the calculator into a given memory location
Data Movement | LOAD | Copy the value from a given memory location into the calculator
Input/Output | INPUT | Get the value from the IN-TRAY and put it into the calculator
Input/Output | OUTPUT | Put the value in the calculator into the OUT-TRAY
Machine Control | STOP | Take a break

## Slide 25: The Little-Man Computer
Let’s see a program in action.

## Slide 26
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0
55

## Slide 27
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55

## Slide 28
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
INBOX --> ACCUMULATOR
INPUT the first number, enter into calculator
55

## Slide 29
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
55
INBOX --> ACCUMULATOR
INPUT the first number, enter into calculator

## Slide 30
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 31
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
ACCUMULATOR
--> MEMORY[08]
STORE the calculator's current value in memory location [08]

## Slide 32
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
ACCUMULATOR
--> MEMORY[08]
STORE the calculator's current value in memory location [08]

## Slide 33
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 34
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
INBOX --> ACCUMULATOR INPUT the second number, enter into calculator

## Slide 35
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
36
INBOX --> ACCUMULATOR INPUT the second number, enter into calculator

## Slide 36
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 37
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
ACCUMULATOR
--> MEMORY[09]
STORE the calculator's current value in memory location [09]

## Slide 38
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
ACCUMULATOR
--> MEMORY[09]
STORE the calculator's current value in memory location [09]

## Slide 39
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 40
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
MEMORY[08] --> ACCUMULATOR
LOAD the first value back into the calculator

## Slide 41
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55
MEMORY[08] --> ACCUMULATOR
LOAD the first value back into the calculator

## Slide 42
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55

## Slide 43
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55
ACCUMULATOR = ACCUMULATOR - MEMORY[09]
SUBTRACT the second number from the first value

## Slide 44
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55-36
ACCUMULATOR = ACCUMULATOR - MEMORY[09]
SUBTRACT the second number from the first value

## Slide 45
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
ACCUMULATOR = ACCUMULATOR - MEMORY[09]
SUBTRACT the second number from the first value

## Slide 46
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 47
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
ACCUMULATOR
--> OUTBOX
OUTPUT the calculator's result to the OUT-TRAY

## Slide 48
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
ACCUMULATOR
--> OUTBOX
OUTPUT the calculator's result to the OUT-TRAY

## Slide 49
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 50
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
Take a break

## Slide 51
In-tray
Out-tray
--
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 52: The Little-Man Computer
The Little-Man doesn’t need to understand the overall goal of the instructions (in this case he doesn’t need to know that he is subtracting two numbers), as long as the boss has arranged the instructions correctly, and the Little-Man follows them, everything works without understanding.
(cf. John Searle's Chinese Room Argument)

## Slide 53: The Little-Man Computer
But, that’s a bit too easy, because the instructions are in plain English.
Let’s make it a bit more complicated
Let’s restate the English as more computer-like instructions.

## Slide 54: The Little-Man Computer
An instruction has two parts – what to do (Operation) and what to do it on (the Operands), e.g.
SUBTRACT Accumulator, [09]

## Slide 55: The Little-Man Computer
An instruction has two parts – what to do (Operation) and what to do it on (the Operands), e.g.
SUBTRACT Accumulator, [09]
Operation

## Slide 56: The Little-Man Computer
An instruction has two parts – what to do (Operation) and what to do it on (the Operands), e.g.
SUBTRACT Accumulator, [09]
Operands
Operation

## Slide 57: The Little-Man Computer
Note:
SUBTRACT Accumulator, [09]
which is
SUBTRACT 55, 36
which is
29

## Slide 58: The Little-Man Computer
So, let’s create codes for different kinds of operations:

## Slide 59: The Little-Man Computer
TYPE OF INSTRUCTION | INSTRUCTION | CODE
Arithmetic | ADD | 1xx
Arithmetic | SUBTRACT | 2xx
Data Movement | STORE | 3xx
Data Movement | LOAD | 5xx
Input/Output | INPUT | 901
Input/Output | OUTPUT | 902
Machine Control | STOP | 000

## Slide 60: The Little-Man Computer
So:
SUBTRACT Accumulator, [09]
becomes
209

## Slide 61: The Little-Man Computer
And:
Becomes: 901, 308, 901, 309,
508, 209, 902, 000
INBOX --> ACCUMULATOR
INPUT the first number, enter into calculator
ACCUMULATOR --> MEMORY[08]
STORE the calculator's current value in memory location [08]
INBOX --> ACCUMULATOR INPUT the second number, enter into calculator
ACCUMULATOR --> MEMORY[09]
STORE the calculator's current value in memory location [09]
MEMORY[08] --> ACCUMULATOR
LOAD the first value back into the calculator
ACCUMULATOR = ACCUMULATOR - MEMORY[09]
SUBTRACT the second number from the first value
ACCUMULATOR --> OUTBOX
OUTPUT the calculator's result to the OUT-TRAY
Take a break
00
01
02
03
04
05
06
07

## Slide 62: The Little-Man Computer
So what does that look like from the Little-Man’s perspective?

## Slide 63
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0
55

## Slide 64
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55

## Slide 65
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
901
55

## Slide 66
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
901
55
55

## Slide 67
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 68
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
308
55
36

## Slide 69
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
308
55
36

## Slide 70
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 71
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
901
55
36

## Slide 72
In-tray
Out-tray
02
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
901
55
36
36

## Slide 73
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 74
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
309
55
36

## Slide 75
In-tray
Out-tray
03
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
309
55
36

## Slide 76
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36

## Slide 77
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
508

## Slide 78
In-tray
Out-tray
04
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
508
55

## Slide 79
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55

## Slide 80
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55
209

## Slide 81
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
55-36
209

## Slide 82
In-tray
Out-tray
05
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
209

## Slide 83
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 84
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19
902

## Slide 85
In-tray
Out-tray
06
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
902
19

## Slide 86
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 87
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
000
19

## Slide 88
In-tray
Out-tray
--
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
55
36
19

## Slide 89: The Little-Man Computer
TYPE OF INSTRUCTION | INSTRUCTION | OP CODE
Arithmetic | ADD | ADD
Arithmetic | SUBTRACT | SUB
Data Movement | STORE | STA
Data Movement | LOAD | LDA
Input/Output | INPUT | INP
Input/Output | OUTPUT | OUT
Machine Control | STOP | HLT

## Slide 90: The Little-Man Computer
But what if we want to do IF statements or WHILE loops, we need some more commands.
We call there “Branch” commands

## Slide 91: The Little-Man Computer
INSTRUCTION | CODE | DESCRIPTION | OP CODE
BRANCH (Unconditional) | Unconditional branch. Set the Program Counter to value XX. | 6xx | BRA
BRANCH IF ZERO | Conditional branch. If the accumulator is zero, branch to XX, otherwise do nothing. | 7xx | BRZ
BRANCH IF POSITIVE | Conditional branch. If the accumulator is positive, branch to XX, otherwise do nothing. | 8xx | BRP

## Slide 92: The Little-Man Computer
So what does a BRA look like from the Little-Man’s perspective?

## Slide 93
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 94
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 95
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
607

## Slide 96
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 97
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
000

## Slide 98
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 99: The Little-Man Computer
So what does a BRZ look like from the Little-Man’s perspective?

## Slide 100
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 101
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 102
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
707

## Slide 103
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
707
36

## Slide 104
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 105
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
308

## Slide 106: The Little-Man Computer
OR

## Slide 107
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 108
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 109
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
707

## Slide 110
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
707
0

## Slide 111
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 112
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
000

## Slide 113
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 114: The Little-Man Computer
So what does a BRP look like from the Little-Man’s perspective?

## Slide 115
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 116
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 117
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
807

## Slide 118
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
807
36

## Slide 119
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 120
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
000

## Slide 121
In-tray
Out-tray
07
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 122: The Little-Man Computer
OR

## Slide 123
In-tray
Out-tray
9
10
11
12
13
14
15
16
18
--
19
1
2
3
4
5
6
7
8
0

## Slide 124
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 125
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
807

## Slide 126
In-tray
Out-tray
00
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
807
0

## Slide 127
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19

## Slide 128
In-tray
Out-tray
01
1
2
3
4
5
6
7
8
9
10
11
13
14
0
12
15
18
16
19
308

## Slide 129: The Little-Man Computer
TYPE OF INSTRUCTION | INSTRUCTION | CODE
Arithmetic | ADD | 1xx
Arithmetic | SUBTRACT | 2xx
Data Movement | STORE | 3xx
Data Movement | LOAD | 5xx
Branching | BRA | 6xx
Branching | BRZ | 7xx
Branching | BRP | 8xx
Input/Output | INPUT | 901
Input/Output | OUTPUT | 902
Machine Control | STOP | 000

## Slide 130: The Little-Man Computer
Let’s say we wanted to write a program to subtract two numbers, but if the first number is smaller than the second one, swap them around, so that the answer is always positive.

## Slide 131: The Little-Man Computer
Get A;
Get B;
Output := A – B;
IF (Output) < 1
THEN Output := B – A;
ENDIF;

## Slide 132: The Little-Man Computer
Get A;
Get B;
Output := A – B;
IF (Output) < 1
THEN Output := B – A;
ENDIF;
INP
STA 10
INP
STA 11
SUB 10
BRP ENDIF;
LDA 10
SUB 11
OUT

## Slide 133: The Little-Man Computer
INBOX --> ACCUMULATOR
INPUT the first number, enter into calculator
ACCUMULATOR --> MEMORY[10]
STORE the calculator's current value in memory location [10]
INBOX --> ACCUMULATOR INPUT the second number, enter into calculator
ACCUMULATOR --> MEMORY[11]
STORE the calculator's current value in memory location [11]
ACCUMULATOR = ACCUMULATOR - MEMORY[10]
SUBTRACT the second number from the first value
IS ACCUMULATOR POSITIVE? GOTO MEMORY[08]
BRANCH to memory location [08] if accumulator is positive
MEMORY[10] --> ACCUMULATOR
LOAD the first value back into the calculator
ACCUMULATOR = ACCUMULATOR - MEMORY[11]
SUBTRACT the second number from the first value
00
01
02
03
04
05
06
07
ACCUMULATOR --> OUTBOX
OUTPUT the calculator's result to the OUT-TRAY
Take a break
[Used for data]
[Used for data]
08
09
10
11

## Slide 134: The Little-Man Computer
INP
STA 10
INP
STA 11
SUB 10
BRP 08
LDA 10
SUB 11
00
01
02
03
04
05
06
07
OUT
HLT
DAT
DAT
08
09
10
11

## Slide 135: The Little-Man Computer
901
310
901
311
210
808
510
211
00
01
02
03
04
05
06
07
902
000
DAT
DAT
08
09
10
11

## Slide 136: The Little-Man Computer
The Little-Man Computer helps explain how the computer works
The Little-Man doesn’t need to know what the program does, it just needs to follow orders.
The Little-Man only does one thing at a time, but the operating system can swap different programs so quickly that it looks like they are all running together.